## Slide 1
IMU-Based Exercise Recognition and Repetition Counter
ECE420 — Embedded Signal Processing Android Application with Real-Time ML Inference

## Slide 2
System Overview
End-to-End Pipeline
• Goal: classify exercise type and count repetitions in real time using only the phone's built-in IMU
• Three target exercises: Biceps Press (BP), Shoulder Press (SP), Triceps Extension (TP)
• Pipeline spans hardware sensing → signal processing → ML training → on-device inference → UI
Four major subsystems:
◦ Sensor layer — Android SensorManager, accelerometer + gyroscope at ~50 Hz
◦ Signal processing — IIR low-pass filter, jerk magnitude, autocorrelation, peak detection
◦ Machine-learning pipeline — offline Python training (sklearn), logistic regression exported to Java
◦ Android application — real-time classification, rep counting, calorie estimation, session history
• All inference runs entirely on-device; no network calls or cloud dependency

## Slide 3
Data Collection Infrastructure
Android IMU Recording Module
• Custom ImuCollector class wraps Android SensorManager and buffers raw sensor events
Two physical sensors registered simultaneously:
◦ TYPE_ACCELEROMETER — linear acceleration in m/s² (ax, ay, az)
◦ TYPE_GYROSCOPE — angular velocity in rad/s (gx, gy, gz)
• Sampling rate: SENSOR_DELAY_GAME (~50 Hz nominal)
• Each event stores event.timestamp in nanoseconds for precise timing reconstruction
Recording session exports a 7-column CSV per set:
◦ timestamp_ms, ax, ay, az, gx, gy, gz
• Export uses ACTION_CREATE_DOCUMENT (Storage Access Framework) — no WRITE_EXTERNAL_STORAGE permission required
• Files collected offline; labeled by folder: data/bp/, data/sp/, data/Triceps/

## Slide 4
Sensor Configuration & Sampling
Hardware Layer Details
• SENSOR_DELAY_GAME is the closest Android constant to 50 Hz (~20 ms event interval)
• Actual rate varies by device; timestamp is used rather than assuming fixed Δt
During active recording all six channels buffered in List<Float> per axis:
◦ accelX, accelY, accelZ — one value per SensorEvent from TYPE_ACCELEROMETER
◦ gyroX, gyroY, gyroZ — one value per SensorEvent from TYPE_GYROSCOPE
◦ accelTs, gyroTs — List<Long> of nanosecond timestamps for each sensor
• Sensor fusion not used; accelerometer and gyroscope are treated as independent channels
• Gravity component is NOT removed — raw accelerometer values are used directly
◦ Gravity provides a stable DC offset that encodes phone orientation, useful for classification
Three parallel ImuCollector instances run simultaneously:
◦ imuCollector — dedicated to rep counting signal
◦ dataCollector — dedicated to CSV file export
◦ liveClassifier — feeds the real-time ML inference module

## Slide 5
Signal Pre-Processing: Low-Pass Filter
IIR First-Order Butterworth Approximation
• Raw accelerometer data contains high-frequency noise from phone vibration and sensor quantization
A causal first-order IIR filter is applied independently to each of the six axes:
◦ y[n] = α · x[n] + (1 − α) · y[n−1]
Filter coefficient α = 0.76, chosen to give a −3 dB cutoff of approximately 14 Hz:
◦ ωc = arccos( 1 − α² / (2(1−α)) )
◦ At fs = 50 Hz: fc = ωc · fs / (2π) ≈ 14 Hz
Why 14 Hz:
◦ Exercise repetition rates fall between 0.3 and 2.5 Hz (fundamental + harmonics up to ~10 Hz)
◦ Cutting at 14 Hz preserves all biomechanically relevant harmonics
◦ Previous value of α = 0.2 (~1.8 Hz cutoff) was too aggressive and distorted rep waveforms
• Filter is applied causally (left-to-right), so no look-ahead latency — suitable for streaming
• Initial condition: y[0] = x[0] (avoids startup transient)

## Slide 6
Jerk Magnitude Computation
Deriving a Periodic Scalar Signal from 3-Axis Data
After filtering, each axis is differentiated discretely to obtain the jerk (rate of change of acceleration):
◦ Δax[n] = ax[n+1] − ax[n]
◦ Δay[n] = ay[n+1] − ay[n]
◦ Δaz[n] = az[n+1] − az[n]
The scalar jerk magnitude collapses all three axes into a single non-negative signal:
◦ J[n] = √( Δax² + Δay² + Δaz² )
Why differentiate before taking magnitude:
◦ Differentiation suppresses the gravity DC offset, making the signal zero-mean around rest
◦ Each repetition produces two distinct jerk peaks (concentric + eccentric phase)
◦ The magnitude operation makes the signal rotation-invariant — result is the same regardless of phone orientation
• Output length is N − 1 samples (one shorter than the input due to differencing)
• Same pipeline applied to gyroscope channels as an alternative rep-counting signal

## Slide 7
Repetition Period Estimation via Autocorrelation
Finding the Dominant Periodicity in the Jerk Signal
• Repetitive exercise produces a quasi-periodic jerk signal; the period corresponds to one full rep
Autocorrelation R(τ) measures self-similarity at lag τ:
◦ R(τ) = (1/T) · Σ_t s(t) · s(t+τ)
◦ where s is the zero-meaned jerk magnitude and T is the number of valid pairs at lag τ
• Zero-meaning is critical: jerk magnitude is always non-negative (DC offset).
• Without zero-meaning, R(τ) is dominated by the constant offset and the true periodic peak is buried
Search range for lag τ:
◦ Minimum: 20 samples ≈ 0.4 s (fastest plausible rep rate)
◦ Maximum: 250 samples ≈ 5.0 s (slowest plausible rep rate)
◦ Upper limit also capped at N/2 to ensure statistical reliability
• The lag τ* with the highest R(τ) is taken as the estimated repetition period L
• L is passed directly to the peak detection stage as the expected rep interval

## Slide 8
Peak Detection Algorithm
Counting Reps from Jerk Peaks
• Peaks in the jerk magnitude correspond to the high-effort phases of each repetition
Three simultaneous criteria must be satisfied for a sample i to be accepted as a peak:
1. Amplitude threshold:
◦ J[i] ≥ mean(J) + 0.4 · std(J)
◦ Rejects low-energy bumps and baseline noise while remaining robust to signal amplitude variation
2. Local maximum:
◦ J[i] > J[j] for all j in [i − L/2, i + L/2], j ≠ i
◦ Window half-width = L/2 ensures only the tallest peak within one half-period is selected
3. Minimum separation:
◦ i − lastAcceptedPeak ≥ L/2 samples
◦ Prevents double-counting a single rep due to a broad or noisy jerk peak
• Final rep count = number of accepted peaks
• Peak indices also used for inter-peak timing to compute average rep cadence (s/rep)

## Slide 9
Repetition Counting Pipeline Summary
Complete Signal Chain
• Stage 1 — Raw IMU: ax, ay, az at ~50 Hz (List<Float>, updated on each SensorEvent)
Stage 2 — IIR Low-Pass Filter (α = 0.76, fc ≈ 14 Hz):
◦ Applied independently to ax, ay, az → smoothed signals fa, fb, fc
Stage 3 — Jerk Magnitude:
◦ Discrete derivative of each filtered axis → L2 norm → scalar J[n]
Stage 4 — Autocorrelation Period Estimation:
◦ Zero-mean J, compute R(τ) for τ ∈ [20, 250], return τ* = argmax R(τ)
Stage 5 — Peak Detection:
◦ Find local maxima in J with minimum separation τ*/2, above mean + 0.4·std
◦ Rep count = number of accepted peaks
Stage 6 — Cadence (s/rep):
◦ avgPeakIntervalSec = mean of consecutive peak-to-peak gaps / 50 Hz
• Identical pipeline available for gyroscope (countRepsGyro); accelerometer used by default

## Slide 10
Feature Extraction: Sliding Window Approach
Bridging Signal Processing and Machine Learning
• Classification requires a fixed-length numerical descriptor of each exercise window
Window parameters:
◦ WINDOW = 100 samples ≈ 2 seconds of motion at 50 Hz
◦ STEP = 50 samples → 50% overlap between consecutive windows
◦ 50% overlap doubles the number of training examples per session
• Each window of 100 samples × 6 channels is reduced to a 46-dimensional feature vector
Three feature families computed per window:
◦ Per-channel statistics (36 features): 6 stats × 6 channels
◦ Magnitude statistics ( 4 features): accel magnitude + gyro magnitude, each with mean & std
◦ Pearson cross-correlations ( 6 features): 6 axis pairs across both sensors
• Feature computation is deterministic and runs on the device in Java, matching the Python training code exactly
• All features are scale-normalized (z-score) before classification using the training-set scaler

## Slide 11
Per-Channel Statistical Features
36 Features — 6 Statistics × 6 Channels
Six statistics are computed from each channel's 100-sample window:
◦ Mean — captures the gravitational and postural DC component
◦ Std — measures the intensity/energy of movement
◦ Min — lower bound of the motion arc
◦ Max — upper bound of the motion arc
◦ Range — Max − Min; total amplitude sweep of the movement
◦ RMS — √(mean(x²)); sensitive to both signal level and variance
• Applied to all six channels in order: ax, ay, az, gx, gy, gz
• This produces 6 × 6 = 36 features occupying indices [0 … 35] of the feature vector
Why include both Std and Range:
◦ Std is sensitive to outliers; Range captures the true excursion; both complement each other
Why include RMS alongside Mean:
◦ For zero-mean signals Std = RMS; for non-zero-mean signals (gravity-biased axes) they diverge,
◦ and RMS captures signal power more accurately than Std alone

## Slide 12
Global Features: Magnitude & Cross-Correlation
10 Features Encoding Multi-Axis Relationships
Magnitude features (indices 36–39) — collapse 3D motion to a scalar signal:
◦ Accel magnitude: ||a||[n] = √( ax² + ay² + az² ) → mean and std over window
◦ Gyro magnitude: ||g||[n] = √( gx² + gy² + gz² ) → mean and std over window
◦ Magnitude is orientation-invariant: same value regardless of phone mount direction
Pearson cross-correlations (indices 40–45) — encode exercise-specific coupling between axes:
◦ r(ax, ay), r(ax, az), r(ay, az) — accelerometer inter-axis correlations
◦ r(gx, gy), r(gx, gz), r(gy, gz) — gyroscope inter-axis correlations
• r(a, b) = Σ(aᵢ−ā)(bᵢ−b̄) / √[ Σ(aᵢ−ā)² · Σ(bᵢ−b̄)² ]
Biological interpretation:
◦ Biceps press has strong az–ay coupling (elbow flexion in the sagittal plane)
◦ Shoulder press has strong ay–az coupling dominated by vertical axis rotation
◦ Triceps extension has a distinct gx–gz gyro signature from elbow extension direction
• Pearson r is bounded [−1, 1] and scale-invariant — robust across subjects of different strength

## Slide 13
Full 46-Dimensional Feature Vector
Index Map
• Indices 0 – 5: ax { mean, std, min, max, range, rms }
• Indices 6 – 11: ay { mean, std, min, max, range, rms }
• Indices 12 – 17: az { mean, std, min, max, range, rms }
• Indices 18 – 23: gx { mean, std, min, max, range, rms }
• Indices 24 – 29: gy { mean, std, min, max, range, rms }
• Indices 30 – 35: gz { mean, std, min, max, range, rms }
• Index 36: accel magnitude — mean
• Index 37: accel magnitude — std
• Index 38: gyro magnitude — mean
• Index 39: gyro magnitude — std
• Index 40: Pearson r( ax, ay )
• Index 41: Pearson r( ax, az )
• Index 42: Pearson r( ay, az )
• Index 43: Pearson r( gx, gy )
• Index 44: Pearson r( gx, gz )
• Index 45: Pearson r( gy, gz )
• Feature vector is identical in Python (train.py) and Java (ExerciseClassifier.java) — any mismatch causes silent accuracy loss

## Slide 14
Dataset Construction & Labeling
Session-Based IMU Recordings
Data collected using the app's built-in CSV recorder across multiple sessions:
◦ Biceps Press (label 0, folder data/bp/) — 6 session files
◦ Shoulder Press (label 1, folder data/sp/) — 6 session files
◦ Triceps Extension (label 2, folder data/Triceps/) — 4 session files
• Each session file: one continuous recording of 10–40+ repetitions
• Session files vary in length; shorter sessions produce fewer windows
Sliding window extraction per session:
◦ WINDOW = 100, STEP = 50 → floor((N − 100)/50) + 1 windows per file
◦ Each window independently labeled with the session's exercise class
• Total dataset: ~400–600 feature vectors depending on recording lengths
Missing data handling:
◦ np.nan_to_num(X, nan=0.0) applied before training
◦ NaN can arise in Pearson r when a channel is constant across the window
• No data augmentation — diversity comes from natural variation across sessions

## Slide 15
Cross-Validation Strategy
GroupKFold — Session-Based Holdout
Standard k-fold cross-validation would cause data leakage in time-series window data:
◦ Adjacent windows from the same session share almost identical samples
◦ A window from session 3 in training and an overlapping window from session 3 in test
◦ would make the test accuracy artifically high and not generalize to new users
• Solution: GroupKFold with groups = session ID
◦ Each fold holds out exactly one complete session as the test set
◦ All windows from that session are withheld from training
◦ No window from a test session ever appears in training — zero leakage
• Number of folds = number of unique sessions (16 total: 6+6+4)
• Each fold trains on 15 sessions, tests on 1 — leave-one-session-out cross-validation
• cross_val_predict aggregates out-of-fold predictions across all folds
• Final reported accuracy/F1 is across all windows, each predicted under a held-out-session regime
• After cross-validation, models are re-fit on the full dataset for deployment

## Slide 16
Classifier Selection: LR and Random Forest
Training & Evaluation
Two classifiers evaluated during development:
Logistic Regression (multinomial, one-vs-rest disabled):
◦ Pipeline: StandardScaler → LogisticRegression(multi_class='multinomial', C=1.0, max_iter=2000)
◦ StandardScaler: z-normalizes each feature to zero mean and unit variance
◦ Multinomial softmax loss over all three classes simultaneously
◦ Regularization strength C=1.0 (L2 penalty) prevents overfitting on small dataset
◦ Closed-form scaler parameters (mean, scale) and LR coefficients (coef, bias) exported to JSON
Random Forest:
◦ RandomForestClassifier(n_estimators=200, max_depth=None)
◦ Serves as a non-linear upper bound on achievable accuracy with these features
◦ Feature importances reported — identifies which of the 46 features matter most
◦ Not deployable to Android (no efficient Java path for tree ensembles)
• Decision: Logistic Regression chosen for on-device deployment
◦ Forward pass is a single matrix multiply + softmax — O(46 × 3) = 138 multiply-adds
◦ Trivially implementable in Java without any ML library

## Slide 17
On-Device Inference Pipeline
Exporting and Running the Classifier in Java
Weight export chain (Python side):
◦ train.py trains LR pipeline, writes weights.json: { bias, mean, scale, coef }
◦ export_weights.py reads weights.json, generates ExerciseClassifier.java with literal float arrays
◦ Generated file replaces the placeholder version in the Android source tree
On-device forward pass (Java side):
◦ Step 1 — Extract 46 features from the current 100-sample window
◦ Step 2 — Z-score normalize: z[i] = (feat[i] − SCALER_MEAN[i]) / SCALER_SCALE[i]
◦ Step 3 — Compute logit per class k: logit[k] = BIAS[k] + COEF[k] · z
◦ Step 4 — Numerically stable softmax: subtract max logit before exponentiation
◦ Step 5 — Predicted class = argmax(probs); confidence = max(probs)
Numerical stability of softmax:
◦ Computing exp(logit[k]) directly can overflow for large logits
◦ Subtracting max(logits) before exponentiation is algebraically equivalent and stays in float range
• No ML framework (TFLite, ONNX) needed — pure Java arithmetic, zero extra APK size

## Slide 18
Real-Time Classification & Idle Detection Gate
LiveClassifier — Streaming Inference Every ~3 Seconds
LiveClassifier runs alongside ImuCollector, processing the rolling sensor buffer:
◦ STEP = 150 samples — classification fires approximately every 3 seconds at 50 Hz
◦ Each inference operates on the most recent 100-sample window (2 seconds)
Two-stage gate before calling the classifier — both must pass:
Gate 1 — Motion energy threshold:
◦ Compute accel magnitude std over the window: σ = std(||a||)
◦ MOTION_THRESHOLD = 0.5 m/s² — rejects stationary or very slow movement
◦ If σ < 0.5: emit null result → UI shows 'Rest', calories = 0
Gate 2 — Periodicity check (rep counter used as detector):
◦ Run SignalProcessor.countRepsAccel() on the same 100-sample window
◦ If rep count < 1: emit null result → UI shows 'Rest', calories = 0
◦ Ensures random aperiodic movement (walking, adjusting equipment) is not classified as exercise
• Only if both gates pass: run ExerciseClassifier.classify() and emit the Result
• Inference runs on a background thread (AsyncTask) to avoid blocking the UI thread

## Slide 19
Calorie Estimation Model
MET-Based Metabolic + Mechanical Work
Two additive components estimate total energy expenditure per session:
Component 1 — Metabolic cost (MET-based):
◦ Calories = MET × body_weight_kg × duration_hours
◦ MET values: Biceps Press = 4.0, Shoulder Press = 5.0, Triceps Extension = 3.5
◦ Body weight entered by user (kg), persisted across sessions via SharedPreferences
◦ Duration = number of confirmed live-classified windows × window_duration
Component 2 — Mechanical work (load-based):
◦ Calories = (load_kg × g × ROM_m × 2 × reps) / (muscle_efficiency × J_per_cal)
◦ load_kg: weight the user reports carrying (dumbbell / barbell)
◦ ROM (range of motion): BP = 0.35 m, SP = 0.55 m, TP = 0.40 m
◦ Factor of 2: accounts for both concentric and eccentric phases
◦ Muscle efficiency ≈ 25%; 1 dietary calorie = 4184 J
Display:
◦ Live panel shows rolling calorie total while exercise is ongoing
◦ During rest/idle: live calories display 0
◦ Session total accumulates across all sets and is shown in the stats bar

## Slide 20
Session Management & User Interface
Multi-Set Workflow
Session lifecycle:
◦ Start button: begins simultaneous IMU collection across all three collectors
◦ Next Set button: freezes current set, processes and logs it, immediately restarts for next set
◦ Stop button: ends collection, runs full rep-counting and stats pipeline, displays results
Set history panel (dynamically populated ListView-style):
◦ Each set entry shows: set number, exercise label, rep count, duration, calories
◦ Color-coded by exercise: Biceps Press = blue, Shoulder Press = green, Triceps Extension = orange
◦ Clear button resets session history
Stats bar (always visible):
◦ Total session duration, average rep cadence (s/rep), peak acceleration (m/s²), cumulative calories
Live detection panel (updates every ~3 s):
◦ Exercise label in class color, softmax confidence percentage, rolling live calorie display
◦ Shows 'Rest / 0 kcal' when either motion or periodicity gate rejects the window
IMU recording panel (independent of rep counting):
◦ Record / Stop buttons save raw CSV at any time via the system file picker
◦ Used during data collection for ML training; unchanged during deployment

## Slide 21
Performance Statistics Displayed to User
On-Device Signal Analysis Results
Rep count:
◦ Derived from peak detection on the jerk magnitude — reported per set and cumulatively
Average rep cadence (s/rep):
◦ avgPeakIntervalSec = mean of peak-to-peak gaps / 50 Hz
◦ More accurate than (total_time / rep_count) because it measures the actual rhythmic interval
◦ Computed from the same autocorrelation → peak pipeline used for counting
Peak acceleration (m/s²):
◦ Maximum accel magnitude sample over the entire set
◦ Reflects the explosive force at the fastest point of the lift
Session duration:
◦ Wall-clock time from Start to Stop, reported in MM:SS format
• All statistics are computed on a background thread after Stop/Next Set is pressed
• UI thread receives results via a Handler post — avoids ANR on long signal buffers

## Slide 22
Three-Class Extension: Adding Triceps Extension
Scaling from Binary to Multinomial Classification
• Initial system: binary classification (Biceps Press vs. Shoulder Press)
• Extension: added Triceps Extension as a third class (label 2)
Changes required in the ML pipeline:
◦ FOLDERS updated: added entry 2 → 'Triceps' pointing to data/Triceps/
◦ LogisticRegression: multi_class='multinomial' already set — no structural change
◦ BIAS vector grows from 2 elements to 3
◦ COEF matrix grows from 2×46 to 3×46
◦ weights.json and ExerciseClassifier.java regenerated by the export script
Changes required in Android:
◦ LABEL_TP = 2, LABEL_NAMES[2] = 'Triceps Extension' added to ExerciseClassifier
◦ labelColor(): TP → deep orange (#E65100)
◦ labelMet(): TP → MET 3.5
◦ getRomM(): TP → ROM 0.40 m
◦ All switch/if chains in RepCounterActivity updated to handle label 0, 1, or 2
• The softmax inference loop is class-count agnostic — loop over N_CLASSES requires no change
• Feature extraction is unchanged — exercise-discriminating information already present in the 46-dim vector

## Slide 23
Key Design Decisions & Tradeoffs
Engineering Choices Made During Development
IIR over FIR for LPF:
◦ IIR uses one coefficient and one state variable — O(1) per sample, minimal memory
◦ FIR would require storing ~50+ past samples for equivalent roll-off
Jerk magnitude over raw magnitude:
◦ Raw accel magnitude is dominated by gravity (~9.8 m/s²); DC bias obscures exercise signal
◦ Differencing removes DC and emphasizes dynamic transitions that mark rep boundaries
Autocorrelation over fixed threshold for period:
◦ Rep rate varies per user and fatigue level; fixed threshold misses slow or fast reps
◦ Autocorrelation adapts the detection window to the actual cadence observed in the data
Logistic Regression over Random Forest for deployment:
◦ LR: 3×46 = 138 floats, one matrix multiply — fits in phone L1 cache
◦ RF: 200 trees × ~1000 nodes each — ~MB of memory + cache-unfriendly traversal
GroupKFold over standard k-fold:
◦ Window overlap between consecutive windows of the same session causes leakage
◦ Session-level holdout gives an honest estimate of generalization to new recording sessions